## Slide 1: Introduction to networking
TCP/IP Five-Layer Network Model
Joel Enrique Esparza Ramirez
Internet of Things

## Slide 2: Lectures
1. Introduction to Networking
2. The Network Layer
3. The transport and application Layer
4. Wireless connections

## Slide 3: Introduction to Networking
TCP/IP Five-Layer Network Model

## Slide 4: TCP/IP Five-Layer Network Model

## Slide 5: Layer 1 physical
Represents the physical devices that interconnect computers

## Slide 7: Layer 2 data link
Responsible for defining a common way of interesting these signals so network devices can communicate

## Slide 8: ethernet
The Ethernet standards also define a protocol responsible for getting data to nodes on the same network

## Slide 9: Layer 3 Network
Allows different networks to communicate with each other through devices known as routers

## Slide 12: internetwork
A collection of networks connected together through routers, the most famous of these being the internet

## Slide 13: Internet protocol
IP is the heart of the internet and most smaller networks around the world

## Slide 14: Client Server

## Slide 15: Layer 4 transport
Sorts out which client and server programs are supposed to get that data

## Slide 17: Osi model

## Slide 18: Introduction to Networking
The basics of networking devices

## Slide 19: cables
Connect different devices to each other, allowing data to be transmitted over them

## Slide 20: Cables
Copper (Spanish)
Fiber (Spanish)

## Slide 21: Cables
The most common forms of copper twisted-pair cables used in networking are Cat5, Cat5e and Cat6 cables

## Slide 23: crosstalk
When an electrical pulse on one wire is accidentally detected on another wire

## Slide 24: Fiber cables
Contain individual optical fibers, which are tiny tubes made out of glass about the width of a human hair

## Slide 26: Recap layer 1

## Slide 27: HUB
A physical layer device that allows for connections from many computers at once

## Slide 28: HUB
A hub is a basic networking device that connects multiple computers or other network devices together. It operates at the physical layer (Layer 1) of the OSI model. When a data packet arrives at one port, it is copied to all other ports so that all segments of the LAN can see all packets.

## Slide 33: Collision domain
A network segment where only one device can communicate at a time

## Slide 34: Collision domain
If multiple systems try sending data at the same time, the electrical pulses sent across the cable can interfere with each other

## Slide 36: Switch
A switch, on the other hand, operates at the data link layer (Layer 2) of the OSI model. It is more advanced than a hub. A switch can inspect the data packets coming in and make decisions about where to send them based on their MAC addresses. Essentially, it can direct packets only to the device that is meant to receive them, rather than broadcasting to all devices.

## Slide 43: Hub and switches
The primary devices used to connect computers on a single network. Usually referred as a LAN, or local area network

## Slide 44: recap

## Slide 45: router
A device that knows how to forward data between independent networks

## Slide 47: Internet service provider

## Slide 49: Border gateway protocol (BGP)
Routers share data with each other via this protocol, which lets them learn about the most optimal paths to forward traffic.

## Slide 50: NODE
A device connected to the network

## Slide 53: The physical layer
Layer 1

## Slide 55: bit
In communication systems, a bit (binary digit) serves as the fundamental unit of data. It represents the smallest piece of information that can be transmitted or processed, which is either a 0 or a 1. These two values correspond to different states, such as on/off, true/false, or any other binary opposition, and are used in various encoding and modulation schemes to represent and convey information over communication channels.

## Slide 56: modulation
A way of varying the voltage of this charge moving across the cable

## Slide 57: Twisted pair cable
The most common type of cabling used for connecting computing devices
It features pair of copper wires that are twisted together

## Slide 59: Duplex communication
The concept that information can flow in both directions across the cable

## Slide 64: T568A/ T568B
T568A Configuration:
Green pair is placed at pins 1 and 2 (White/Green, Green)
Orange pair is placed at pins 3 and 6 (White/Orange, Orange)
T568B Configuration:
Orange pair is placed at pins 1 and 2 (White/Orange, Orange)
Green pair is placed at pins 3 and 6 (White/Green, Green)

## Slide 65: Network ports

## Slide 66: DATA LINK layer
Layer 2

## Slide 68: ETHERNET
Ethernet is widely used in various network setups, from simple home networks connecting a few devices to complex corporate data centers with thousands of connections. It provides a reliable and standardized way to network devices with different capabilities.

## Slide 69: CSMA/CD
Carrier Sense Multiple Access with Collision Detection (CSMA/CD) is a network protocol for carrier transmission that is used in Ethernet networks to control access to the network medium. It's a fundamental part of the Ethernet standard for handling situations where two or more devices attempt to send data at the same time, leading to a collision.

## Slide 70: NIC
A Network Interface Card (NIC), also known as a network card, network adapter, or LAN adapter, is a piece of computer hardware designed to allow computers to communicate over a computer network. It provides the physical interface between a computing device and the network cable, and it is a critical component for establishing a network connection.

## Slide 71: MAC
A MAC address, short for Media Access Control address, is a unique identifier assigned to network interfaces for communications on the physical network segment. MAC addresses are used as a network address for most IEEE 802 network technologies, including Ethernet and WiFi. Essentially, it helps in ensuring that the physical devices in a network can be uniquely identified and communicated with.

## Slide 72: FORMAT
A MAC address is typically a 48-bit (6-byte) or, in some cases, a 64-bit (8-byte) number. The 48-bit address is most commonly used and is represented in hexadecimal notation, divided into pairs (e.g., 00:1A:2B:3C:4D:5E).

## Slide 73: Assignment
MAC addresses are usually assigned to the network interface card (NIC) by the manufacturer at the time of production, and thus they are also referred to as hardware addresses or physical addresses. The first half of the MAC address represents the manufacturer's unique identifier (also known as the Organizationally Unique Identifier - OUI), and the second half is the serial number assigned by the manufacturer.

## Slide 75: ETHERNET MAC
Ethernet uses MAC addresses to ensure that the data is sends has both and address for the machine that sent the transmission, as well as the one the transmission was intended for.

## Slide 76: Unicast
Unicast is a one-to-one type of communication. In unicast, data packets are sent from a single source to a single destination with a unique address. It is the most common form of data transmission on the Internet.

## Slide 77: Multicast
Multicast is a one-to-many type of communication. In multicast, data packets are addressed to a specific group of destination computers simultaneously. Only the devices that have joined a specific multicast group will receive the multicast packets.

## Slide 78: Broadcast
Broadcast is a one-to-all communication method. In broadcast, data packets are sent from a single source to all possible destinations within the network segment or domain. Every device on the network receives the broadcast packets but only processes them if they are of interest; otherwise, they are discarded.

## Slide 80: DATA PACKET
A data packet, often simply referred to as a "packet," is a formatted unit of data carried by a packet-switched network. In the context of computer networks, a packet is a small segment of a larger message or stream of data that’s transmitted over a network.

## Slide 81: ETHERNET FRAME
An Ethernet frame is a specific structure used for framing data packets in Ethernet networks. It encapsulates the data packet for transmission over an Ethernet link. The frame structure is defined by various IEEE standards, with the most common being IEEE 802.3.

## Slide 83: Preamble and Start Frame Delimiter (SFD)
Preamble (7 bytes): A sequence of alternating 1s and 0s that allows devices on the network to easily synchronize their receiver clocks, providing a buffer to establish bit-sync for the actual frame.
Start Frame Delimiter: Signals the beginning of the frame data with a specific byte pattern (10101011), marking the end of the preamble and the start of the Ethernet frame.

## Slide 84: Destination MAC Address
The Media Access Control (MAC) address of the intended recipient of the frame. This could be a unicast (single device), multicast (group of devices), or broadcast (all devices) address.

## Slide 85: Source MAC Address
The MAC address of the sender of the frame. This is used by the receiving device to know where the frame originated from.

## Slide 86: EtherType/Length
EtherType: When used as EtherType, this field indicates the protocol of the encapsulated data packet, allowing the receiving device to properly interpret the payload.
Length: Alternatively, it can signify the length of the payload in bytes.

## Slide 87: Payload
The actual data being transported. This includes any headers for other protocols carried within the Ethernet frame, such as an IP packet.

## Slide 88: Frame Check Sequence
A cyclic redundancy check (CRC) used for error checking. The FCS allows the receiver to detect some types of errors in the transmission. If the FCS does not match the calculated value, the frame is discarded.

## Slide 89: NETWORK layer
Layer 3

## Slide 91: IP
The Internet Protocol (IP) is a set of rules governing the format of data sent over the Internet or other networks. IP is a fundamental protocol within the Internet protocol suite, which is a collection of networking protocols that includes TCP, UDP, and many others.

## Slide 92: IP
Dynamic
Static

## Slide 93: Static IP Addresses
A static IP address is a fixed address that is manually assigned to a device and does not change over time. Once a device is assigned a static IP address, that address remains the same until it is manually changed, or the device is removed from the network.

## Slide 94: Usage
Static IP addresses are typically used for devices that need to maintain the same IP address for an extended period, such as servers, network printers, or other devices that need to be reliably accessed by the same IP address. They are also used for DNS servers, VPN gateways, and devices that require remote access.

## Slide 95: Dynamic IP Addresses
A dynamic IP address is assigned to a device for a limited period or until the device disconnects from the network, using a DHCP server. When the lease for an IP address expires, the device may be assigned a new IP address.

## Slide 96: Usage
Dynamic IP addresses are commonly used for consumer devices, such as personal computers, smartphones, and tablets connected to a residential internet connection, or devices in corporate environments that do not require permanent IP addresses.

## Slide 97: IPV4
IPv4, or Internet Protocol version 4, is the fourth revision of the Internet Protocol (IP) and a widely used protocol in data communication over different kinds of networks. IPv4 is the first version of the protocol to be widely deployed, and it forms the basis for most of the Internet's current architecture.

## Slide 98: 32-bit Addressing
IPv4 addresses are 32 bits long, which allows for a theoretical maximum of about 4.3 billion unique addresses (2^32). However, large blocks of addresses are reserved for special uses and cannot be allocated for public internet routing, reducing the number of addresses available for general use.

## Slide 99: Address Notation
IPv4 addresses are typically expressed in dotted-decimal format, which divides the 32-bit address into four 8-bit fields. Each field is then represented as a decimal number (ranging from 0 to 255) and separated by periods. For example, 192.168.1.1 is a standard representation of an IPv4 address.